## Slide 1: Improving Safety through better Communication
Notes: INTRODUCTION
ALL CLEAR? is the name given to several products aimed at raising awareness of the importance of air-ground communications and some of the problems that can arise when such communication breaks-down.
The ALL CLEAR? learning concept is to promote discussions by pilots and controllers about how communication problems occur, how they can be avoided, or dealt with, and to provide an environment where personal experiences can be shared with colleagues.
A EUROCONTROL Air-Ground Communications Safety Initiative was launched in 2003 with a statistical study of hundreds of incident reports and a corresponding safety survey of pilots and controllers. This Initiative was supported by airline and air traffic associations, pilot and controller organisations and the flight safety foundation.
The results of the study and survey are published in the 2006 Action Plan, which includes detailed Briefing Notes. One of the objectives in the Action Plan was to raise awareness across the Industry – which has resulted in ALL CLEAR?
LESSON
This power-point presentation is a short introduction to the European Air - Ground Communications Action Plan just covering some of the main points and it is intended as a preliminary to other ALL CLEAR? resources such as the Video clips and on-line computer-based learning.
After a short introduction (about 5 minutes) we will:
Watch some (1, 2, 3, or 4) film clips of communication scenarios based on actual events and acted out in real-time; then discuss what we observe, ways of preventing similar errors and any similar personal experiences you may have had in the past
Finish with several more slides (about 10 minutes) in order to tie up loose ends and provide some recommended practices
Training Option – for briefing on company, local and state communication SOPs, or any other additional material as required and appropriate.
Overall this training session will take …………… minutes.
There will/wont be handouts at the end.
Next Slide – why is communication so important, what can the consequences be when communication breaks down?

## Slide 2: Importance of Communications
Communication problems are the most
common causal factor in Runway Incursions
There are 2 Runway Incursions everyday somewhere in Europe
Notes: When we talk about air-ground communications, we do not exclude ground operations of aircraft.
In fact the existing risks on the ground are probably the highest – a ground collision can be catastrophic.
Runway Incursions – 2 a day throughout Europe - of course not all of these incursions are critical, but this indicates what the real exposure is and potential risk.
Communication problems are the most common causal factor in runway incursions.
Q: Are we just concerned here with aircraft?
Q: How does communication breakdown contribute to runway incursions?
Q: Are there any examples of accidents due to runway incursion that have occurred strictly due to communication problems?
Next Slide – It’s not just collisions on the ground we should worry about: What is another potential catastrophic situation?

## Slide 3: Importance of Communications
Communication problems are the most
common causal factor in Level Busts
There are an estimated 10 Level Busts per day in Europe
1 in 10 Level Busts results in a loss of separation <1nm
Notes: Level Busts.
Most common causal factor.
You can see that there are hundreds of level busts each year in Europe for which communication error is the main cause and in which separation distances become unacceptable.
Summarise – So the impact of poor or failing communication is to increase the risks of collision on the ground and in the air – a situation we should not accept. For the sake of adhering to clear standards and simple practices, and through sharing our experiences, we can reduce these risks considerably.
Next Slide – It is worth now taking a look at some examples which demonstrate how a skill we use all day, and often take for granted, can frequently let us down.

## Slide 4: ALL CLEAR? VIDEOS Four short films to be discussed
Call-sign Confusion
Radio Discipline
Blocked Transmission
Loss of Communication
Notes: TRAINING OPTION
Delete this slide if you do not intend to “show” the video film scenarios
Amend it if you only intend showing some of the film clips, or
Move the slide to a place in the power-point presentation that is convenient for you.
Notes:
Use the High definition versions of the films – available on DVD from EUROCONTROL
You may find the transcripts helpful to clarify any misunderstandings – although if students cannot hear every word clearly this just reflects on our own inability to hear everything – all the time, which makes a point!
You may wish to use the video commentaries in facilitating the session.
Also see Instructions for Trainers document for ideas on facilitating the discussions.
Run the films …….

## Slide 5: Importance of Communications
Quality of Communications
Pilot and Controller Workload
Military
interception
CFIT
Runway
Incursion
Level
Bust
Loss of
separation
Airspace
penetration
Distraction
De-confliction
action
Extra
coordination
Increasing Risks
Notes: We have seen in these short films, and probably experienced first-hand, how our quality of communications, or our communication performance decreases with increasing workload.
The opposite is also true – that is, when our communication performance is reduced (for some reason) our workload increases as we try to resolve the issue. This process can be a downward spiral.
Q: What effect does poor quality communication have on Pilots’ and Controllers’ workloads?
Extra coordination
De-confliction action
Distraction
Using up TIME and ………….. time = DISTANCE
All this can divert attention from other safety critical tasks!
We’ve already seen the statistics for Runway Incursions and Level Busts;
Q: What other risks can arise due to the affects of poor quality communication?
As well as runway incursions and level busts, poor communication can lead to:
    Loss of separation
    CFIT?
    Loss of communication – military intercept (this involves a lot of controller resources and time)
    Unauthorised penetration of airspace (incorrect clearances flown)
Hence the importance of applying standard communication processes which ease the workload by ensuring communication between pilots and controllers is standard and effective, and that errors are recognised as they occur and corrected immediately.
Next Slide – what process do we routinely apply (perhaps without thinking, and sometimes incomplete) every time we communicate via radio?

## Slide 6: Making ourselves understood
The Communication Loop:
Read-back and hear-back errors account for
over 30% of identified communication problems.
Notes: THE COMMUNICATION LOOP
Read-back and Hear-back are essential to good communications; when they are used they provide an effective quality check as a safety net.
For The Communication Loop to be effective both controllers and pilots must not only LISTEN effectively, but
be totally DISCIPLINED in their use of R/T and radio equipment. Ideally read-back should involve READING and Hear-back should involve HEARING (or if you prefer LISTEN-BACK and WRITE DOWN) – not just going through the motions.
Short substitutions for full read-backs only prevent the safety net of controller hear-back from operating, and also encourages controllers to omit acknowledgements of read-backs.
Q: What words or phrases do we sometimes use which break the safety net of a full read-back and subsequent hear-back?
A: Wilco, Roger, or just our Call-sign/identifier, etc ….(Discuss)
Q: In what other ways can the communication loop breakdown?
Q: How can we ensure that the communication loop is always completed fully?
Next Slide - Working within the procedure of the Communication Loop we also have to make our best effort to be understood when we SPEAK.

## Slide 7: Communication Performance
CLARITY
Pace
Accent
Pronunciation
Volume
Tone
Measured
Clear
Constant
Neutralised
Conversational
Notes: The most direct influence we have on communication performance, specifically whether other people understand us or not, is of course how we speak.
CLARITY
Q: what characteristics of our speech can we change to affect other people’s ability to understand us?
ICAO even prescribes recommendations for each of these characteristics.
Q: how should we control these speech characteristics so as to be better understood and avoid confusion?
Pace - speed must allow a clearance to be written down - avoid speeding up when frequency is congested – leads to more errors and frequency time sorting it out. - Measured
Volume – Keep it constant. Use a head set, and don’t turn your head away from mic, and don’t shout! - Constant
Pronunciation - Use your jaw, tongue and teeth – overcome laziness, put some effort into it! - Clear
Accent - Even for native English speakers, some localised accents will not be understood by non-native English speakers. - Neutralised
Tone - Make it natural and conversational – that’s what people expect – when urgency needs to be conveyed, or when an unusual clearance or request is made, a change to this conversational tone will “highlight” the information. - Conversational
Next Slide – Even if we speak very clearly so that the receiver catches every word exactly – how else are we prone to creating chaos and confusion from our communication?

## Slide 8: Communication Performance
Avoiding Ambiguity:
Do not read-back clearance as a question
ASK!
Not Sure?
“Say again for Alert123”
What, Where, When?
“Was that FL 140
for Distracted123?”
“She did say left onto
240, didn’t she?”
“To Paris 121.3
Unsure789?”
Use Standard
Phraseology
Notes: AMBIGUITY
Q: How do we usually avoid ambiguity?
A: Always use Standard phraseology!
Even using standard phraseology we can still create confusion Q: How can we reduce ambiguity further?
A: Restrict elements in each message – emphasise unusual words and phrases – pronounce digits separately – pause slightly before and after frequencies – specify millibars/flight level/degrees/feet – don’t say “er” where it isn’t needed – never pass headings ending in 0 or 5? Etc ….
Discuss phrases and words that can be (and often are) misinterpreted eg: TO and TWO; FOR and FOUR, ‘270’ is that degrees of Flight Level?; GO AHEAD; BEHIND; AFTER; NINER and FIVER
Beware - Conditional Clearances are traps for ambiguity – discuss how conditional clearances are given and how they should be read back.
Q: If we are unsure what it is we have just heard – What should we do? and What shouldn’t we do?
Never assume, unless you assume it is wrong!
The important thing is that whenever you are uncertain about something – CHECK IT – Ask!
Do not use the read-back to ask a question (even on the flight deck between pilots)
Often people who are unsure read back in an enquiring tone of voice ie “rising tone at end of the sentence” this just encourages the controller to accept the read-back (as expected) and ignore, or to instantly confirm as correct.
In the same way confirmatory questions (leading questions) just invite people to answer “yes” and not really listen.
Make the other person THINK, Ask an open question
Always check understanding by asking an open question or giving a command to repeat something – remember to emphasise your call-sign it this was in doubt.
Next Slide – It is not just the message content that can cause ambiguity, but if the wrong aircraft picks up a message meant for someone else the consequences can be severe.

## Slide 9: Communication Performance
Avoiding Ambiguity:
Do not clip transmissions
Always use full call-sign unless instructed by ATC
Always inform if potential call-sign confusion identified
Call-sign Confusion is a major reason for
aircraft taking the wrong clearance
Notes: Call-sign Confusion is the major reason for aircraft taking a clearance not intended for them, and this confusion can last for several exchanges of communication between the air and ground, thereby introducing a degree of ambiguity.
NB: This confusion for controllers can be visual as well as aural/phonetic.
Q: In what ways do call-signs become confused?
Common prefixes and suffixes dilute their effectiveness and adds to potential confusion, eg. one in five call-signs use the word “AIR”, many others have similar derivatives eg “AERO”.
Using a consecutive numbering system will increase the likelihood of confliction
Discuss local problems and company experiences of call-sign confusion. Is it a big problem? Yes? - Then inform the Safety Office!
NB: Similar sounding call-signs in the same sector increases the potential for simultaneous transmissions.
NB: EUROCONTROL CFMU is studying ways of allocating call-signs pre-flight where potential conflicts are forecast. Until such a system is in place …..
Q: What measures can be taken to reduce the chances of call-signs being misheard:
? …..discuss
Avoid clipped transmissions
Shortened and partial call-signs - only use when instructed by ATC to use shortened version or temporary alternative
Not knowing what other call-signs are on frequency – ATCOs should also inform adjacent sectors.
Next Slide – Confusing call-signs can lead to the wrong aircraft taking the wrong clearance, and if unnoticed a loss of communication.

## Slide 10: Communication Performance
Loss of Communication:
Do not combine frequency changes with any other clearance
Pause before switching frequencies – listen for corrections to read-back
After selecting new frequency pause before speaking
Monitor 121.5
Return to previous frequency when necessary
Frequency changing is a major catalyst for loss of communication
Notes: Frequency Changes = one of the most common reasons for loss of communication, either because the read-back/hear-back process failed and an incorrect frequency was set, or as often occurs frequency changes happen at the limit of reception.
Discuss company experiences of loss of communications:
Q: Is there a common factor?
Q: Are company SOPs effective? NO? – tell someone!
Etc…….
Q: How can we reduce the risks of loss of communication at, or after, a frequency change?
ATC - Transmit frequencies on their own (ATC) – with no other clearance
Pilots - Pausing before a frequency change provides an opportunity for a confirmation or correction to the read-back,
Pilots – Pausing after selecting a new frequency prevents a simultaneous/blocked transmission on first call
If range is an issue – ensure that clearances and frequencies are passed well in advance.
Q: How can we recover the situation if we do lose communication?
Use and monitor 121.5
Return to previous frequency
Consider using a “relay”.
Training Option – you may wish to discuss company SOPs for lost comms, military intercepts and also sleeping receivers (if this is a problem).
Next Slide – “Blocked transmissions”

## Slide 11: Communication Performance
Blocked Transmissions:
Avoid pausing in the middle of a message
Do not release press-to-transmit switch before finished transmitting
Be alert for your own call-sign
Number of incidents increasing
Notes: Also an increasing occurrence is the number of simultaneous and therefore blocked transmissions – mainly due to congested frequencies, but perhaps partly due to poor discipline.
Q: What are the potential consequences of Blocked/Simultaneous Transmissions?
A: mainly the unnoticed failure of the Communication Loop by one or more parties and subsequent flying of incorrect clearance(s) by one or more aircraft.
Training Option – reference to the 1977 runway collision at Tenerife (KLM and PANAM)
Q: What can we do with our own discipline to improve the situation?
Next Slide – basically many of the problems we encounter can be reduced by adherence to ……(communication loop)

## Slide 12: Communication Performance
Stop talking
Eyes down – concentrate
Write it down!
Beware of
EXPECTATIONS and
making ASSUMPTIONS
The Communication Loop
Effective Listening:
Notes: …… the communication loop.
To do this requires Effective Listening!
Q: How can we enhance our listening performance?
A: Stop talking - Concentrate (eyes down!) – avoid distractions –– write clearances down.
Writing down clearances will assist our performance accuracy and will:
  Help listening concentration
  Overcome short-term memory failure
  Assist accurate read-back (thereby reducing radio traffic/frequency congestion)
  Provide a record.
Relying on our short term memories is a losing strategy!
Q: What is one very common reason why we think we heard something, when another thing completely different was said (not just at work)?
A: Assumptions and Expectations.
Listening carefully and writing down clearances should prevent us from routinely making assumptions based on our expectations.
Next Slide – Having worked on our own communication performance, there is a way that we can be doubly vigilant……

## Slide 13: Communication Performance
Teamwork:
Cross-check
Monitor
Don’t distract
Crew/Team
Resource
Management
Reduce and
Share
Workload
Use of Technology
Notes: TEAMWORK
Using our colleagues as a safety net is essential during critical phases of an operation and especially when the work load is high. Even SOPs can be considered as another team-mate.
NB: if the SOPs are well-written, then they should emphasise and encourage teamwork (especially on the flight deck).
Similarly supervisory practices in the control room can be used to reduce the chances of communication error.
SOPs can also offer guidelines on communication management to reduce risks.
In particular the procedures for setting frequencies, headings and flight levels; monitoring frequencies and recording clearances and cross-checking our colleagues.
Knowing the importance of communication we should monitor our own self distraction and distraction of/by colleagues.
As well as colleagues and SOPs we can utilise the set-up of displays whether in the cockpit or on the HMI to assist in reducing communication errors.
The more that is known about our experiences of communication errors
Then the more we will know about why they occur and
How they can be avoided
Always REPORT REPORT REPORT!!!
Next slide – That is the end of this short presentation; but there is a lot more detail in other ALL CLEAR? products ……

## Slide 14: More
Visit ALL CLEAR?
www.allclear.aero
Notes: If you wish to learn more, and/or revise what we have spoken about today then access the ALL CLEAR? web-site for more resources.
Training Option – companies may require all controllers/pilots to undertake the on-line web-based training, which takes up to 30 minutes and is accessible through the all clear website.
NB: Trainers may wish to give handouts at this stage such as ALL CLEAR top tips, AGC Action Plan Briefing Notes or any local material available.
Next Slide - Questions

## Slide 15: is that… ALL CLEAR?
if not ask a question!
Notes: QUESTIONS
Next 2 Slides – optional top 5 tips for Pilots and Controllers.

## Slide 16: Communication Tips
Top 5 Tips for Pilots:
  Do not read back clearances as questions
  Check R/T if there is a prolonged break in activity on frequency
  When reading back a conditional clearance, state the condition first
  Set the clearance given, not the clearance expected
  If you are unsure - always check
Notes: Training Option to show this slide – depending on handouts or amend for own circumstances

## Slide 17: Communication Tips
Top 5 Tips for Controllers:
  Frequency changes should be kept separate from other instructions
  Avoid issuing more than two instructions in one transmission
  If it is urgent – sound urgent
  Avoid distractions – especially the telephone
  If you are unsure - always check
Notes: Training Option to show this slide – depending on handouts or amend for own circumstances